## Slide 1: Phased array patch antenna @10GHz
Objective: “Design a 1D patch phased array of 10 elements with corporate feeding network for broadside radiation, target return loss is -10 dB. Calculate the radiation pattern analytically and numerically and compare them. If you want you can select the operating frequency yourself, otherwise use 10 GHz.”
Khai NGUYEN - Oct. 2022

## Slide 2: Stack-up
Find an industrialized stack-up so that the design can be fabricated.
4-layer stack-up allows having thin substrate, hence thin feeding microstrip line.
RO4350B chosen for lower dielectric loss

## Slide 3: Intended design
The patch array antenna is designed as follow:
  Broadside direction toward +Z
  Feeding comes from –Y toward +Y
  Array’s elements placed 1D along X and have distance

## Slide 4: Analytical estimation of 1x10 patch array

## Slide 5: Analytical analysis of the array
Cavity model of the element patch antenna
TM010 as dominant mode
The following is MATLAB calculation from Balanis for the intended design (chapter 14)
INPUT PARAMETERS
================
RESONANT FREQUENCY (in GHz) = 10.0000
DIELECTRIC CONSTANT OF THE SUBSTRATE = 3.6600
HEIGHT OF THE SUBSTRATE (in cm) = 0.0254
POSITION OF THE RECESSED FEED POINT (in cm) = 0.2000
OUTPUT PARAMETERS
=================
PHYSICAL WIDTH OF PATCH (in cm) = 0.9827
EFFECTIVE LENGH OF PATCH (in cm) = 0.8027
PHYSICAL LENGH OF PATCH (in cm) = 0.7785
E-PLANE HPBW (in degrees) = 136.0000
H-PLANE HPBW (in degrees) = 80.0000
DIRECTIVITY OF RECTANGULAR PATCH (dimensionless) = 4.2200
DIRECTIVITY OF RECTANGULAR PATCH (in dB) = 6.2531
RESONANT INPUT RESISTANCE AT LEADING RADIATING EDGE (y=0) Rin0= 293.4669 ohms
RESONANT INPUT RESISTANCE AT RECESSED FEED POINT (y=0.2000 cm) RINYo= 140.3699 ohms
*** NOTE:
THE E-PLANE AMPLITUDE PATTERN IS STORED IN Epl-Micr_m.dat
THE H-PLANE AMPLITUDE PATTERN IS STORED IN Hpl-Micr_m.dat
=========================================================

## Slide 6: Analytical analysis of the array
Analytical pattern calculated by Balanis for X-direction broadside
E-plane ()
H-plane()
E-plane ()
H-plane ()

## Slide 7: Analytical analysis of the array
The symmetry of the antenna allows us to have now
  E-plane ()
  H-plane()
Rotating along Y-axis to achieve the intended +Z broadside patch antenna.
E-plane ()
H-plane ()

## Slide 8: Analytical analysis of the array
Array factor of the patch array along X axis
Broadside direction is along +Z
with , and is phase difference between neighbor elements.
So
z
x

## Slide 9: Analytical analysis of the array

## Slide 10: Numerical estimation of 1x10 patch array

## Slide 11: Patch array design
Using online tool to calculate patch dimension.

## Slide 12: Numerical simulation CST
Recessed microstrip-line feed point to have a better impedance matching
Making array with distance /2 = 15mm and with separate ports
Phase excitation is controlled by simulator
Microstrip line width is 0.53mm
7.75mm
2mm
2mm
9.82mm
Single patch design
1x10 patch array design

## Slide 13: Numerical simulation CST
Simulation of single patch
7.75mm
2mm
2mm
9.82mm
Single patch design
Impedance matching of single patch
3D radiation pattern of single patch

## Slide 14: Numerical simulation CST
Simulation of single patch
7.75mm
2mm
2mm
9.82mm
Single patch design
E-plane
H-plane

## Slide 15: Numerical simulation CST
Simulation of single patch versus analytical results
  Directivity = 6.62 dBi (versus 6.25 dBi of analytical result)
  E-plane HPBW = 134.8o (versus 136o of analytical result)
  H-plane HPBW = 86.6o (versus 80o of analytical result)
7.75mm
2mm
2mm
9.82mm
Single patch design
*back radiation due to finite ground plane

## Slide 16: Numerical simulation CST
Simulation of 1x10 patch array ()
E-plane
H-plane
Array directivity

## Slide 17: Numerical simulation CST
Simulation of 1x10 patch array ()
E-plane
H-plane
Array directivity

## Slide 18: Numerical simulation CST
Simulation of 1x10 patch array ()
E-plane
H-plane

## Slide 19: Comparison
Full analytical result from MATLAB calculations of patch pattern and array factor
Main lobe at
Beamwidth
Directivity 16.2 dBi
Partially analytical result from numerical patch pattern and MATLAB calculation array factor
Close to full analytical results
Full numerical result of the array. Electric boundary is used as ground so there is no back radiation
Main lobe at
Beamwidth
Directivity 14.8 dBi

## Slide 20: Comparison
Full analytical result
Main lobe at
Beamwidth
Directivity 16.2 dBi
Partially analytical result
Close to full analytical results
Full numerical result
Main lobe at
Beamwidth
Directivity 14.7 dBi

## Slide 21: Comparison
Full analytical result
Main lobe at
Beamwidth
Directivity 16.2 dBi
Partially analytical result
Close to full analytical results
Full numerical result
Main lobe at
Beamwidth
Directivity 14.8 dBi

## Slide 22: Conclusion
The numerical results of separating-element array are quite close to either full or partial analytical results if we ignore the back radiation (depends on ground plane side), in terms of
  Direction of main lobe
  Direction and number of nulls
  Beamwidth
  Directivity
  Sidelobe level
The asymmetry of the feed, the finite dimension of the ground in simulation can introduce some differences in the single element pattern and hence array pattern.

## Slide 23: Design of feeding network

## Slide 24: Feeding network
To produce the difference in phase excitation of each element of the array we can
  Use some active components, such as phase-shifter.
    Normally requires complicated control.
    Need to design a DC part that doesn’t couple with RF part
  Passive feeding network, like
    Butler matrix, need power-two (2x) number of input and output
    Rotman lens allows have any number of antenna port.

## Slide 25: Rotman lens for feeding network
10 array ports (connect to antennas)
9 beam ports (excitation ports)
8 dummy ports ( loads)
30o phase shift to cover

## Slide 26: ROTMAN import CST
Phase differences are not perfectly produced as intended by the Rotman lens
  Excitation of port 5:
  Excitation of port 4 and 6:
  Excitation of port 3 and 7:
  …
All ports have better Return Loss than -12dB
Expecting up to 6dB loss due to the Rotman lens

## Slide 27: Final design
Some microstrip line phase-shifters are introduced and optimized to produce a phase balance at every antenna port.
Simulation takes long time on a 16Gb RAM laptop and cannot run very fine meshes.

## Slide 28: Final design
Some microstrip line phase-shifters are introduced and optimized to produce a phase balance at every antenna port.
Simulation takes long time on a 16Gb RAM laptop and cannot run very fine meshes.

## Slide 29: Results
Excitation to Port 5
Main lobe at
3dB beamwidth
Directivity 14.24 dBi
Excitation to Port 4
Main lobe at
3dB beamwidth
Directivity 14.07 dBi
Excitation to Port 3
Main lobe at
3dB beamwidth
Directivity 14.42 dBi
Excitation to Port 2
Main lobe at
3dB beamwidth
Directivity 14.1 dBi
Excitation to Port 1
Main lobe at
3dB beamwidth
Directivity 14.2 dBi

## Slide 30: Results
All ports have better matching than -10dB
The antenna can scan 60o broadside with around 14 dBi of directivity and with better than 5.5 dB total loss.
Directivity and HPBW of each beam in the final design are similar to that of analytical and separating element design.
Phase difference is smaller and varying making the scanning range smaller.
Because the feeding network is not perfect, the pattern is not clean as the analytical synthesis or numerical result in which there is no feeding network.

## Slide 31: Perspective
This is a preliminary design, refinements are required on
  Fine mesh simulations
  Optimizing the Rotman lens to obtain step
  Optimizing the microstrip phase-shifters
  Finalize the feeding ports to SMA

## Slide 32: References
Eurocircuits site: https://www.eurocircuits.com/
Balanis, “Antenna Theory: Analysis and Design,” 4th edition, MATLAB code: https://fr.mathworks.com/academia/books/antenna-theory-balanis.html
Rotman lens design using MATLAB: https://fr.mathworks.com/matlabcentral/fileexchange/50490-rotman-lens-design-with-hfss-link?s_tid=mwa_osa_a
Patch dimension calculator: https://www.pasternack.com/t-calculator-microstrip-ant.aspx
Microstrip line calculator: https://www.pasternack.com/t-calculator-microstrip.aspx

## Slide 33: Annex: Analytical analysis of the array
Array factor of the patch array along X axis
Broadside direction is along +Z
with , and is phase difference between neighbor elements.
So
z
x